## Slide 1
Verification Method
For
VLSI Design
By
Saikot Das Joy
A Presentation on

## Slide 2
VLSI stands for “Very Large Scale Integration”
Process of creating integrated circuits (ICs):
=> contain a very large number of transistors
=> ICs are used in a wide variety of electronic devices
Verification : an essential part of the VLSI design process
=> ensure that the ICs that are created will function correctly
Importance
Of Verification
Complexity
Time and Cost
Reliability
Quality
Introduction
There are different methods of VLSI Design Verification. We will talk about it.
Notes: VLSI design verification is important for several reasons:
Quality: Verification helps ensure that the VLSI design is of high quality and will function correctly when it is fabricated. This is important because defects in VLSI designs can be very costly to fix, and may even result in the entire design process having to be repeated. By verifying the design, designers can identify and fix problems before the design is sent for fabrication, which can help improve the quality of the final product.
Time and cost: Verification can save time and money by identifying problems early in the design process. Fixing a problem after the design has been fabricated can be much more time-consuming and costly than fixing it during the design phase. By verifying the design before it is sent for fabrication, designers can avoid these costly delays.
Complexity: VLSI designs can be very complex, with millions of transistors and other components. Verification helps ensure that all of these components are working together correctly and that the design meets all of the specified requirements.
Reliability: Verification can help improve the reliability of VLSI designs by identifying and fixing problems before the design is sent for fabrication. This can help reduce the risk of failure and improve the overall performance of the final product.
In summary, VLSI design verification is an essential step in the design process that helps ensure the quality, reliability, and cost-effectiveness of the final product.

## Slide 3
VLSI Design Process
Requirement Gathering
System Level Design
Microarchitecture Design
Logic Design
Physical Design
Verification
Fabrication
Testing
Notes: The VLSI design process is a complex, multi-step process that involves several different activities. Here is an overview of the main steps in the VLSI design process:
Requirements gathering: In this step, designers work with customers and other stakeholders to gather and understand the requirements for the VLSI design. This includes defining the functionality and performance of the device, as well as any constraints or limitations.
System-level design: In this step, designers create a high-level system-level design of the VLSI device, which defines how the different components of the device will fit together and interact.
Microarchitecture design: In this step, designers create a detailed microarchitecture design of the VLSI device, which defines the specific components that will be used and how they will be interconnected.
Logic design: In this step, designers create the logic design of the VLSI device, which defines the specific logic functions that will be implemented in the device. This is typically done using a hardware description language (HDL) such as VHDL or Verilog.
Physical design: In this step, designers create a physical layout of the VLSI device, which defines the specific locations and sizes of the components on the chip.
Verification: In this step, designers use various methods (e.g. simulation, formal verification, hardware emulation) to verify that the design is correct and meets all of the specified requirements.
Fabrication: In this step, the VLSI design is sent to a foundry where it is fabricated using photolithography and other processes.
Testing: After the VLSI device has been fabricated, it is tested to ensure that it is functioning correctly and meets all of the specified requirements.
These are the main steps in the VLSI design process, although the specific activities and order of steps may vary depending on the specific design and the tools and methods being used.

## Slide 4
Verification Method for VLSI Design
Functional Verification
Static Timing Analysis (STA)
Formal Verification
Simulation Based Verification
Verification Method for VLSI Design
There are various methods of describing VLSI design
Verification.
Commonly used methods are the functional method, performance verification, power-aware
method, clocking, CDC verification, DFT verification,FPGA/emulation, HW co-verification, etc.
Functional verification method and emulation are the
most widely used methods.
And Another type : Static Timing Analysisis- is the path of
design timing that validates the timing performance. STA
is commonly used to determine signal delay and timing
performance violations. It determined the full circuit behavior
with the best vector outputs
We will mainly focus on Functional Verification and Emulation
on this Presentation

## Slide 5
Approaches of Functional Verification
Black Box
White Box
Gray Box
+
=
There are three approaches for Functional Verification

## Slide 6
Formal Verification
A method of verifying the correctness of a VLSI design using mathematical methods and techniques.
Involves expressing the design and its requirements as a set of formal, logical statements, and using automated tools to prove that the design meets these requirements.
Can be used to prove the correctness of a design at any level of abstraction, from the highest level system-level design down to the lowest level gate-level design
Different formal verification tools available, including JasperGold, Spyglass, and Questa Formal.
=>These tools allow designers to express the design and its requirements in a formal language, and to use automated methods to prove that the design meets these requirements.
Formal Specifications
Formal Tool
DUT
Done
Counter Example
Pass?
Yes
No

## Slide 7
Simulation-Based Verification
A method of verifying the functionality of a VLSI design using computer simulations.
involves creating a model of the design using a hardware description language (HDL) such as VHDL or Verilog:
=>using a simulation tool to test the design by applying a series of stimuli (inputs) and observing the resulting responses (outputs).
typically used to test the functionality of a VLSI design at different levels of abstraction:
=> from the highest level system-level design down to the lowest level gate-level design.
It helps ensure that the design is correct and meets all of the specified requirements.
Different simulation-based verification tools available, including VCS, ModelSim, and Questa.
=>These tools allow designers to create and run simulations of their designs, and to debug and fix any problems that are found.
Generates Stimulus
Reference Model
DUT
Check Results

## Slide 8
Emulated Verification
Emulation is the method of performing the functional verification
of the hardware and software of the design by automatically
mapping the design’s RTL representation to its internal
programmable gate array using a specialized computer.
it provides information about synthesis, power, timing, area, and other constraints that are
not covered by simulation verification, this process improves our level of detail and understanding
of the chip.
We usually emulate the design into an FPGA(Field Programmable Gate Array)

## Slide 9
Static Timing Analysis
A method used to verify the timing performance of a VLSI circuit design.
Involves analyzing the design to determine the delay of signals as they pass through the circuit:
=> ensures the specified timing constraints
number of tools available for performing static timing analysis of VLSI designs. Some of the most common include:
(a)Timing analyzers (b)Timing constraint editors
©Timing-aware synthesis tools (d) Timing simulation tools etc.

## Slide 10
DIGITAL CIRCUIT
--- 11
--- 00
--- - -
--- - -
--- 01
COMPARATOR
10 ---
00 ---
- - ---
- - ---
01 ---
Stored Correct Response
TEST RESULT
INPUT PATTERNS
OUTPUT RESPONSES
VLSI Testing
VLSI Testing Flow
Types of Testing
Incoming Inception
Production
Burn-In
Characterization
Types of VLSI Testing
Notes: 1. Characterization: It is a design debug verification process
before being sent to production that verifies all specifications
are correct. SEM and AI are some common tools used in
testing that depicts the limits of operating values. We measure
the data statistically to ensure the testing by taking average
data or getting pass/fail results indicates the good testing
format.
2. Production: Production tests, which are performed on every
fabricated chip but are less thorough than characterization
tests, are still required to maintain quality standards by determining
whether the device meets specifications
3. Burn-In: the production reliability of chips should be
checked by the Burn in process. We put the chips through a
combination of production tests, high temperatures, and overvoltage
power supplies during burn-in.
4. Incoming inception: This testing’s primary objective is to
avoid installing a defective component in a system assembly,
where diagnosing the problem could cost much more than
performing an initial inspection.

## Slide 11
Tools for VLSI Design Verification
Primetime:
- Static timing analysis tool
- Ensuring design integrity
- Accurate signoff analysis
- Power and variation
aware analysis
Innovus:
- Design, stimulate and synthesis
- Design rule check
with verification facilities
- lay out and parasitic
capacitance verification
- available in working
CR-500:
- used in design for ICs
complex speed boards
- improve in signal integrity
- electromagnetic compatibility
Mentor Graphics:
- Creates advanced ICs
- Optimal balance power facilities
- validation process
active in all levels
- have the Si life cycle method
for ensuring safety
-Deliver Coverage, and
high resolution
Power Artist:
- generate CAD and CAM
- Design rule checking process
fast and efficient data sharing
- Use in Multiphysics simulation
Pathwave:
- Electromagnetic simulation
- Yielding with optimization
- To make nonlinear design
- visualization of the physical layout

## Slide 12
Choosing Right Verification Method
Type of Design
Design Complexity
Time and Resources
Industry standards
Cost
several factors to consider when choosing a verification method for VLSI
the right verification method for VLSI design will depend on the specific characteristics of the design, as well as the time, resources, and budget available for verification.
Different verification methods are suitable for different types of designs. For example, functional verification is suitable for verifying the functionality of a design, while physical verification is suitable for checking the layout of a design.
The complexity of the design will also influence the choice of verification method. For complex designs, a combination of different verification methods may be required.
The time and resources available for verification will also be a factor in choosing a verification method. Some methods may be more time-consuming or resource-intensive than others.
It is important to consider any relevant industry standards or guidelines when choosing a verification method.
The cost of the verification method should also be considered, including both the upfront cost and any ongoing maintenance or support costs.

## Slide 13
References
https://www.wallpaperflare.com/central-processing-unit-cpu-hardware-digital-art-computer-wallpaper-powqu
https://unsplash.com/photos/49uySSA678U
https://sigosa.de/wp-content/uploads/2017/06/gold-Industriegold-564790.jpg

## Slide 14
Any Questions?